## Slide 1
Feroze1888 Mills Limited
Check Sheet
A convenient and compact format for data collection
A Simple rule– Maximum information with minimum writing efforts and easy to fill

## Slide 2
Feroze1888 Mills Limited
Check Sheet

## Slide 3
Feroze1888 Mills Limited
Graphs & Charts
Graphs represent data pictorially. A picture can see what 1000 words can not tell.
We have different types of charts, few common types are given below.
Line Chart
Bar Chart
Multiple bar chart
Pie Chart
Gantt chart etc..

## Slide 4
Feroze1888 Mills Limited
Graphs & Charts
Line Graph
Line graphs manifest the overall trend in time series data by direction of their lines.
Bar chart
Bar graphs are parallel bars of identical width but differing length to compare size of different quantities / things.
Pie Chart
Pie charts makes it easy to grasp the breakdown of the components of a quantity over a certain period.

## Slide 5
Feroze1888 Mills Limited
Graphs & Charts
Multiple Bar Chart
Used for the comparison purpose. Like to compare the production of Machine A & B
Component Bar Chart
Used for comparison as well as to show contribution
Chart: Machine A Vs Machine B
Machine A | 4 | 8 | 7 | 15 | 16 | 20 | 14
Machine B | 5 | 10 | 5 | 12 | 15 | 18 | 15
Chart: 
Machine A | 4 | 8 | 7 | 15 | 16 | 20 | 14
Machine B | 5 | 10 | 5 | 12 | 15 | 18 | 15

## Slide 6
Feroze1888 Mills Limited
Graphs & Charts
Gantt Chart
Gantt Charts makes it easy to understand the details of a plan and progress in its implementation schedule.
Type of work | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Foundation work Frame work Dry-walling Exterior touch up Sheetrock work Plumbing Electrical wiring Fit Fixtures Paint interior wall Interior touch up Inspection delivery |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 7
Feroze1888 Mills Limited
Pareto Diagram
80% of problems are caused by less than 20% of probable causes.
Establishes proof of the need.
Identifies vital few.

## Slide 8
Feroze1888 Mills Limited
Pareto Diagram
Example: Personal Expense
Head | Expense | Ratio to total | Comm. Frequency
Eidi | 4500 | 28.3% | 28.3%
Dress | 4000 | 25.2% | 53.5%
Perfume | 4000 | 25.2% | 78.6%
Shoes | 2400 | 15.1% | 93.7%
Others | 1000 | 6.3% | 100.0%
Total | 15900 |  | 

## Slide 9
Feroze1888 Mills Limited
Pareto Diagram
Solution by Minitab: Step by Step
Head | Expense | Ratio to total | Comm. Frequency
Eidi | 4500 | 28.3% | 28.3%
Dress | 4000 | 25.2% | 53.5%
Perfume | 4000 | 25.2% | 78.6%
Shoes | 2400 | 15.1% | 93.7%
Others | 1000 | 6.3% | 100.0%
Total | 15900 |  | 
Step 1 : Open Minitab
Step 2 : Enter Data

## Slide 10
Feroze1888 Mills Limited
Pareto Diagram
Solution by Minitab: Step by Step
Head | Expense | Ratio to total | Comm. Frequency
Eidi | 4500 | 28.3% | 28.3%
Dress | 4000 | 25.2% | 53.5%
Perfume | 4000 | 25.2% | 78.6%
Shoes | 2400 | 15.1% | 93.7%
Others | 1000 | 6.3% | 100.0%
Total | 15900 |  | 
Step 3 : Go to Stat Menu > Quality Tools > Pareto Chart
Step 4 : A window will appear to select data

## Slide 11
Feroze1888 Mills Limited
Pareto Diagram
Solution by Minitab: Step by Step
Head | Expense | Ratio to total | Comm. Frequency
Eidi | 4500 | 28.3% | 28.3%
Dress | 4000 | 25.2% | 53.5%
Perfume | 4000 | 25.2% | 78.6%
Shoes | 2400 | 15.1% | 93.7%
Others | 1000 | 6.3% | 100.0%
Total | 15900 |  | 
Step 5 : A Pareto Chart will appear
Step 6 : Analyse the Chart

## Slide 12
Feroze1888 Mills Limited
Cause & Effect Diagram
Graphic tool to represent relationship between an effect and influencing causes.
There can not be an effect without a cause.
Reduce incidence of subjective decision making.
Identify main causes X’s influencing Y.
For each of the X’s identified in the fishbone diagram classify them as follows:
Controllable – C (Knowledge)
Procedural – P (People, Systems)
Noise – N (External or Uncontrollable)
First produced in 1950 by Professor Kaoru Ishikawa - Also called the:
  Ishikawa Diagram
  Fish Bone Diagram

## Slide 13
Feroze1888 Mills Limited
Construction of C&E Diagram
Define problem
Gather members for discussion
Conduct Brainstorming
Group causes into 6M’s for Product and 4P’s and 2M’s for the Services
For each cause, ask, “What goes wrong that produces the effect”.
Identify major causes
Product: 6M’s
Man
Machine
Material
Method
Mother-nature
Measurement
Services: 5M’s & 1E
People
Policy
Procedure
Place
Measurement
Mother-nature

## Slide 14
Feroze1888 Mills Limited
Cause & Effect Diagram
Failure
Effect
Failure Mode
(Defect)
Measurements Materials Manpower
Mother Methods Machines Nature

## Slide 15
Feroze1888 Mills Limited
Example 1: C &E Diagram (Defects)
Measurement
Reproducibility
Repeatability
Linearity
Stability
Calibration
Methods
Vague
Out of date
Complex
Machines
Not maintained
Inadequate capability
Material
Late
Wrong quantity
Defective
Manpower
Inadequate training
Lack of experience
Distractions
Mother nature
Too humid
Too hot
Too cold
Defects

## Slide 16
Feroze1888 Mills Limited
Activity#3
Your car is consuming a lot of Petrol. In a group of two, construct a fish bone diagram to capture all possible causes for this nausea .

## Slide 17
Feroze1888 Mills Limited
High Petrol
Consumption
Procedure
Driver
Vehicle
Materials
Maintenance
Road
Restrictions
No turn
One way
Circuitous
Road
Frequent
stops
Crossings
Traffic
Speed Breakers
Steep
Poor
condition
Potholes
Irregular
servicing
False
economy
Negligence
Clogged
filters
Low pressure
Ignorance
Faulty
pressure
Tyres
Petrol
Oil
Not changed
Low level
Incorrect viscosity
Impurities
Incorrect
Octane no.
Additives
Spares
Spurious
Inferior
Impatience
Craze
Always
late
Riding on
clutch
Lack of
awareness
Poor
anticipation
Wrong
gears
Poor
skill
Wrong
culture
Bad
attitude
Inexperience
Body
Heavy
Shape
Technical
details
Carburetor
Spark plugs
Life
Contacts
Fuel mix
Engine
High H.P
Cylinders
Activity 3: C &E Diagram

## Slide 18
Feroze1888 Mills Limited
Histogram
A Histogram is a bar graph that shows frequency data.
Histograms provide the easiest way to evaluate the distribution process.
Histogram is characterized by 3 Constituents:
Center ( mean)
Width (spread-variation)
Over all shape

## Slide 19
Feroze1888 Mills Limited
Exercise: Histogram
Plot the histogram of Supplier 1 from the data given in camshaft. Mtw.
Step 1 : File > Open Worksheet > camshaft. mtw

## Slide 20
Feroze1888 Mills Limited
Histogram
Step 2 : Graph > Histogram > Simple

## Slide 21
Feroze1888 Mills Limited
Histogram

## Slide 22
Feroze1888 Mills Limited
Types of Histogram
Bell Shaped
Symmetrical shape with a peak in middle representing a normal histogram.
Skewed to Left
Caused by centering the process toward high end of the tolerance.
Skewed to Right
Caused by centering the process toward low end of the tolerance.

## Slide 23
Feroze1888 Mills Limited
Types of Histogram
Bimodal
Two combined populations-- two shifts, operators, inspectors, suppliers, machine settings, gages, tools, machines, measurement locations, etc.
Truncated
This can happen when a process is not capable of meeting the specifications, parts are sorted from both ends, or too few classes are chosen.
Missing Centre
Centre of the distribution has been sorted from the rest. Portion may have been delivered to a customer with tighter specifications.

## Slide 24
Feroze1888 Mills Limited
Histogram in Process Behavior
It tells whether process is under control?
Is it producing defect free output?
USL
LSL
process variability
LSL
USL

## Slide 25
Feroze1888 Mills Limited
Histogram in Process Behavior
Shape close to normal curve
Mean at target value
Spread within Specification limits
Cp is greater than 1.67 and Cpk is greater than 1.33

## Slide 26
Feroze1888 Mills Limited
Scatter Diagram
What: To study the possible relationship between two variables.
Why: Diagram make it clear whether a relationship exists, and shows the strength of relationship.
When: To test a theory that the 2 variables are related.

## Slide 27
Feroze1888 Mills Limited
Example: Scatter Diagram
Length | Weight
5.5 | 62
5 | 58
5.2 | 60
5.8 | 68
5.7 | 70
5.6 | 63
5.1 | 61
5.1 | 63
5.4 | 70
6 | 75
5.9 | 68
6.1 | 78
5.3 | 60
5.6 | 65
5.7 | 68
5.8 | 68
5.4 | 64
6 | 75
5.3 | 69

## Slide 28
Feroze1888 Mills Limited
Scatter Diagram
Solution by Minitab: Step by Step
Step 1 : Open Minitab
Step 2 : Enter Data

## Slide 29
Feroze1888 Mills Limited
Scatter Diagram
Solution by Minitab: Step by Step
Step 3 : Select Graph > Scatter Plot
Step 4 : Select With Regression

## Slide 30
Feroze1888 Mills Limited
Scatter Diagram
Solution by Minitab: Step by Step
Step 5 : Choose X and Y Variables
Scatter Plot

## Slide 31
Feroze1888 Mills Limited
Interpretation of Plots
Strong Positive
Weak Positive
None
Strong Negative
Weak Negative
Curvilinear

## Slide 32
Feroze1888 Mills Limited
Control Chart
The control chart is a graph used to study how a process changes over time. Data are plotted in time order.
A control chart always has a central line for the average, an upper line for the upper control limit and a lower line for the lower control limit.
Lines are determined from historical data. By comparing current data to these lines, you can draw conclusions about whether the process variation is consistent (in control) or is unpredictable (out of control, affected by special causes of variation).

## Slide 33
Feroze1888 Mills Limited
When to use Control Chart?
  Controlling ongoing processes by finding and correcting problems as they occur.
  Predicting the expected range of outcomes from a process.
  Determining whether a process is stable (in statistical control).
  Analyzing patterns of process variation from special causes (non-routine events) or common causes (built into the process).
  Determining whether the quality improvement project should aim to prevent specific problems or to make fundamental changes to the process.

## Slide 34
Feroze1888 Mills Limited
Important Terminologies
Common Causes of Variation
Consists of combined effect of several sources of uncontrollable variation inherent to a process.
Special Causes of Variation
Determination of source of impact makes cause "assignable." and is termed as assignable cause of variation.
Specification Limit
Limits defined by the customer. Voice of customer
Control Limit
Measures the variation of sample statistics by using data points.

## Slide 35
Feroze1888 Mills Limited
Common & Special Causes
Special Cause
Special Cause
Common Cause
UCL
LCL
CL